## Slide 1: RELATED WORK
The Maximum Likelihood Estimation (MLE)
Subspace-Based Approaches (MUSIC AND ESPRIT)
Sparse Signal Reconstruction (SSR)
Machine Learning (ML)
Notes: O aprendizado de máquina (ML) é apresentado como uma tecnologia promissora para ser usada para DOA. Os métodos baseados em ML são orientados por dados e, portanto, podem ser mais robustos do que outros métodos, pois se adaptam melhor às imperfeições da geometria da matriz e às imperfeições do sensor. Eles também não dependem da forma da geometria da matriz [20]. Além disso, o ML oferece implementação e simplicidade de baixo custo.

## Slide 2
References | Azimuth | Elevation | Single source | Multi sources | Narrowband | Wideband
(Liu, 2018) |  | x |  | x | x | 
(Terabayashi, 2014) |  | x |  | x |  | x
(Xia, 2015) | x |  | x |  | x | 
(Kase, 2018) |  | x |  | x | x | 
(Barthelme, 2020) | x |  |  | x | x | 
(Guo, 2020) | x |  |  | x | x | 
(Huang, 2018) | x |  | x |  | x | 
(Abeywickrama, 2018) | x |  | x |  | x | 
(Pastorino, 2005) |  | x | x | x | x | 
(Randazzo, 2007) |  | x | x | x | x | 
(Donelli, 2009) | x | x | x | x | x | 
(Pan, 2017) |  | x |  | x | x | 
(Huang, 2019) |  | x |  | x | x | 
(Wu, 2019) | x |  | x |  | x | x
Notes: pode-se concluir que as técnicas gerais de ML podem oferecer melhores métodos de DOA do que os mencionados acima. ML tem sido usado principalmente para melhorar o ângulo de azimute ou a resolução do ângulo de elevação e a velocidade de computação. Além disso, vários estudos foram realizados para encontrar o endereço de várias fontes. No entanto, o estudo da abordagem de resposta completa DOA baseada em ML (conhecimento do azimute e do ângulo de elevação) não foi profundamente estudado. O motivo é o grande tamanho dos dados de treinamento que não são suportados por todos os modelos, como NN. No entanto, a estimativa dos ângulos de elevação e azimute é crucial e tem muitas aplicações em vários campos da engenharia. Por exemplo, com uma informação DOA completa, é possível melhorar a cobertura de transmissão nas comunicações sem fio, evitando interferências e aumentando a capacidade do sistema. Mais especificamente, o conhecimento do azimute e do ângulo de elevação traria um melhor aproveitamento da tecnologia BF nas redes móveis de próxima geração.

## Slide 3: OBJECTIVES
The main objective of this work is to propose a ML model to find the azimuth and elevation angle of a signal coming from. To achieve the latter, the following specific objectives are considered:
  Design an antenna system to find DOA.
  Discuss training data preparation and designing for a specific scenario.
  Analyze different proposals to find both angles with ML models.
  Analyze different ML models.
  Select the best proposal to find the azimuth angle and elevation angle as well as the ML model from simulation results.
Notes: O aprendizado de máquina (ML) é apresentado como uma tecnologia promissora para ser usada para DOA. Os métodos baseados em ML são orientados por dados e, portanto, podem ser mais robustos do que outros métodos, pois se adaptam melhor às imperfeições da geometria da matriz e às imperfeições do sensor. Eles também não dependem da forma da geometria da matriz [20]. Além disso, o ML oferece implementação e simplicidade de baixo custo.

## Slide 4
The system consists of a single channel receiver, equipped with direction antennas.
The receiver activates one antenna element sequentially at a time () using the corresponding switch and received energy value.
Single Channel SDR
N-element Directional Antenna Array
Single-pole-N-throw
Antenna Switch
Machine Learning
SYSTEM MODEL
Notes: Consideramos um sistema que consiste em um receptor de canal único e um conjunto de antenas circulares equipadas com antenas de direção N, veja a Fig. 1
O conjunto de antenas está conectado ao receptor usando um comutador RF SPNT (Single-Pole-N-Throw) não reflexivo. O período de troca é Ts. Suponha que um sinal de drone de campo distante colide com o conjunto de antenas com o ângulo de azimute ∈ [0 2pi). O sinal recebido no n-ésimo elemento da antena pode ser dado como (1). SPNT = Interruptor de antena de polo único N-throw
O método proposto é o seguinte.
O receptor ativa seqüencialmente um elemento de antena de cada vez usando o comutador RF SPNT e mede o valor de energia recebido correspondente. Durante a ativação da n-ésima antena, Pn é medido, onde n ∈ {1, · · ·, N}. Um único ciclo de comutação é equivalente a N ativações, iniciando da primeira antena à N-ésima antena.
Seja p = [P1, · ·, PN] ote denotar as medições de potência correspondentes a um único ciclo de comutação.
We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 5
Data generation
Set input parameters: ,
Calculate [x]:
Calculate [xx ]:
Calculate [xx ]:
i
: random number between 10 meters and 1 km
Calculate [xx ]:
Quero encontrar os ângulos com base na potência medida em cada uma das antenas de um conjunto de antenas
Um conjunto de antenas posicionadas de forma circular.
Considerar a equação de transmissão de Friis na m-ésima antena de recepção:
END
Premissas:
Antena de transmissão seja isotropica, sem perdas (=1).
A antena de recepção esteja no campo distante da antena de transmissão.
Notes: We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 8
Set input parameters: ,
Calculate [x]:
Calculate antenna_cordinates [3]:
i
: random number between 10 meters and 1 km
Calculate :
Calculate the coordinates of the source:
Calculate the distance between the source and each of the antennas:
Calculate the angles between the source and each of the antennas:
n
END
yes
no
yes
yes
no
no
yes
no
Notes: We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 9
Set input parameters: ,
Calculate [x]:
Calculate antenna_cordinates [3]:
i
: random number between 10 meters and 1 km
Calculate :
Calculate the coordinates of the source:
Calculate the distance between the source and each of the antennas:
Calculate the angles between the source and each of the antennas:
n
END
yes
no
yes
yes
no
no
yes
no
Notes: We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 10
Set input parameters: ,
Calculate [x]:
Calculate antenna_cordinates [3]:
i
: random number between 10 meters and 1 km
Calculate :
Calculate the coordinates of the source:
Calculate the distance between the source and each of the antennas:
Calculate the angles between the source and each of the antennas:
n
END
yes
no
yes
yes
no
no
yes
no
Notes: We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 11
Set input parameters: ,
Calculate [x]:
Calculate antenna_cordinates [3]:
i
: random number between 10 meters and 1 km
Calculate :
Calculate the coordinates of the source:
Calculate the distance between the source and each of the antennas:
Calculate the angles between the source and each of the antennas:
n
END
yes
no
yes
yes
no
no
yes
no
Notes: We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 12
Set input parameters: ,
Calculate [x]:
Calculate antenna_cordinates [3]:
i
: random number between 10 meters and 1 km
Calculate :
Calculate the coordinates of the source:
Calculate the distance between the source and each of the antennas:
Calculate the angles between the source and each of the antennas:
n
END
yes
no
yes
yes
no
no
yes
no
Notes: We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 13
Set input parameters: ,
Calculate [x]:
Calculate antenna_cordinates [3]:
i
: random number between 10 meters and 1 km
Calculate :
Calculate the coordinates of the source:
Calculate the distance between the source and each of the antennas:
Calculate the angles between the source and each of the antennas:
n
END
yes
no
yes
yes
no
no
yes
no
Notes: We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 14
Initial Dataset
Pre-processed Dataset
Training set
Validation set
Train model
label_predict
+
i
Count +=1
Count =0
yes
no
yes
no
Evaluate model performance (accuracy)
Data splitting
Machine Learning (accuracy)
Notes: We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 15
Simulation Results
The azimuth and elevation angles are in a range of [:) and [:) respectively with an angle resolution of . Hence the data samples are formed by the corresponding power received at each antenna () and the direction information . For each angle pair, 400 samples were generated. In this way, the total number of data generated is 5184000 () to each antenna.
Notes: Consideramos um sistema que consiste em um receptor de canal único e um conjunto de antenas circulares equipadas com antenas de direção N, veja a Fig. 1
O conjunto de antenas está conectado ao receptor usando um comutador RF SPNT (Single-Pole-N-Throw) não reflexivo. O período de troca é Ts. Suponha que um sinal de drone de campo distante colide com o conjunto de antenas com o ângulo de azimute ∈ [0 2pi). O sinal recebido no n-ésimo elemento da antena pode ser dado como (1). SPNT = Interruptor de antena de polo único N-throw
O método proposto é o seguinte.
O receptor ativa seqüencialmente um elemento de antena de cada vez usando o comutador RF SPNT e mede o valor de energia recebido correspondente. Durante a ativação da n-ésima antena, Pn é medido, onde n ∈ {1, · · ·, N}. Um único ciclo de comutação é equivalente a N ativações, iniciando da primeira antena à N-ésima antena.
Seja p = [P1, · ·, PN] ote denotar as medições de potência correspondentes a um único ciclo de comutação.
We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 16
Decision Tree Classifier
Random Forest Classifier
Simulation Results: Learning curves

## Slide 17
DOA estimation as a classification problem
Find the angle of azimuth and the angle of elevation independently: The problem of DOA estimation is divided into two independent classification problems: One to find the azimuth angle and the other to find the elevation angle.
Find the azimuth angle and the elevation angle with the same ML model instance.
Find the azimuth angle and the elevation angle with ML model multilabel, and multioutput.
First proposal | Second Proposal | Third Proposal
Set for the azimuth angle: Set for the elevation angle: | Set that combines azimuth angle with elevation angle | Set for the azimuth angle: Set for the elevation angle:
First proposal | Second Proposal | Third Proposal
Notes: Consideramos um sistema que consiste em um receptor de canal único e um conjunto de antenas circulares equipadas com antenas de direção N, veja a Fig. 1
O conjunto de antenas está conectado ao receptor usando um comutador RF SPNT (Single-Pole-N-Throw) não reflexivo. O período de troca é Ts. Suponha que um sinal de drone de campo distante colide com o conjunto de antenas com o ângulo de azimute ∈ [0 2pi). O sinal recebido no n-ésimo elemento da antena pode ser dado como (1). SPNT = Interruptor de antena de polo único N-throw
O método proposto é o seguinte.
O receptor ativa seqüencialmente um elemento de antena de cada vez usando o comutador RF SPNT e mede o valor de energia recebido correspondente. Durante a ativação da n-ésima antena, Pn é medido, onde n ∈ {1, · · ·, N}. Um único ciclo de comutação é equivalente a N ativações, iniciando da primeira antena à N-ésima antena.
Seja p = [P1, · ·, PN] ote denotar as medições de potência correspondentes a um único ciclo de comutação.
We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)

## Slide 18
Metrics and scoring
First proposal | Second Proposal | Third Proposal
First proposal | Second Proposal | Third Proposal
Notes: Consideramos um sistema que consiste em um receptor de canal único e um conjunto de antenas circulares equipadas com antenas de direção N, veja a Fig. 1
O conjunto de antenas está conectado ao receptor usando um comutador RF SPNT (Single-Pole-N-Throw) não reflexivo. O período de troca é Ts. Suponha que um sinal de drone de campo distante colide com o conjunto de antenas com o ângulo de azimute ∈ [0 2pi). O sinal recebido no n-ésimo elemento da antena pode ser dado como (1). SPNT = Interruptor de antena de polo único N-throw
O método proposto é o seguinte.
O receptor ativa seqüencialmente um elemento de antena de cada vez usando o comutador RF SPNT e mede o valor de energia recebido correspondente. Durante a ativação da n-ésima antena, Pn é medido, onde n ∈ {1, · · ·, N}. Um único ciclo de comutação é equivalente a N ativações, iniciando da primeira antena à N-ésima antena.
Seja p = [P1, · ·, PN] ote denotar as medições de potência correspondentes a um único ciclo de comutação.
We consider a system which consists of a single channel receiver, and a circular antenna array equipped with N direction antennas, see Fig. 1. The antenna array is connected to the receiver using a non-reflective Single-Pole-N-Throw (SPNT) RF switch.By processing the signals that are transmitted from the drone to its ground controller, the single channel receiver measures the received signal power at the each antenna using a RF switching mechanism.
Then, the obtained power values are fed to the proposed sparse denoising autoencoder (SDAE)-based deep neural network (DNN). More precisely, the first hidden layer of the network extracts a robust sparse representation of the received power values. Then, the rest of the network utilizes this sparse representation to classify the direction of the drone signal.
Since they consider a practical DF method in this paper, 𝑎_𝑛 (𝜃) and 𝑠(𝑘)